Technical Report
 on
 TELESET-ABCCOM

 Document specifying current status and future development of

TELESET-ABCCOM Software Chain

Raju Uparade

Naresh Sisodiya

Charu Kanade

Jitendra Kodilkar

GMRT - TIFR

INDEX

- What was there
- What we did
- What needs to be done
- How we should proceed

What was there

TELESET - ABCCOM was developed by Mr. Lorrent Pommier along with Mr. Pramesh Rao

TELESET
SHARED MEMORY

TELEDISP

MULTI SERIAL PORT
@ 9.6 kbps

ABCCOM

SERVO SYSTEM

MCM DEVICE
DRIVER

RS-422 comm
@ 9.6 kbps

RS-485 comm
@ 9.6 kbps

IF/LO/FPS/FE/SENTINEL

Figure shows what was developed earlier

- TELESET-ABCCOM is developed using C++ and C which is very tightly coupled code.
- All communications were @ 9.6 kbps.
- Whole software was developed on Fedora Core – 3 ( kernel version 2.6.9)

   What we did

TELESET
SHARED MEMORY

IF/LO/FPS/FE/SENTINEL

Ethernet( TCP/IP
@ 100 Mbps
TELEDISP

ABCCOM

SERVO SYSTEM

MCM DEVICE
DRIVER

RS-422 comm
@ 9.6 kbps

RS-485 comm
@ 9.6 kbps

Figure shows what modification and development we did

Work done on TELESET – ABCCOM software chain

- Communication link between TELESET-ABCCOM changed from serial to Ethernet (TCP/IP @100Mbps).
- Whole software chain including MCM device driver ported to FC9, FC16 and Ubuntu 11.04.
- Alternate Server design and Bit extraction code written for TELESET.
- Modified Teleset and Abccom for Sentinel System (Temperature Monitoring).
- Testing of all software in Telemetry Lab, Servo Lab, FE Lab ,ABR Lab and at Antenna Base.
- Successfully tested whole software chain at C00,C04 And C12 during maintenance period.
- Had problem with LO Monitoring, modified the software,now can fully control and monitor all Antenna sub-systems.
- Software fine Tuning And Optimization:
DOMON time prior modification:

LO Domon ( Not working)
IF Domon	30 sec
FE Domon	20 sec
FPS Domon	10 sec

DOMON time after modification:

LO Domon (Working)	15 sec
IF Domon	20 sec
FE Domon	10 sec
FPS Domon	5 sec

SEN Domon	5 sec

- Successfully tested Teleset and Abccom at C12 Antenna after software fine tuning & optimization.
- Mr. Madhav Mishal build combined RS- 485 & RS-422 converter card which is driven by taping power from USB port, successfully tested the circuit in C00, C04 and C12 antennas.
- We have tested the USB to Serial port interface card in C00, C04 and C12 by sending commands to servo system and getting the required acknowledgment.
- Teleset and Abccom software tested successfully in Lab with rabbit program on serial communication.
What need to be done

Control & Monitor
GUI

CEB
Control & Monitoring
 System

Correlator

Pulsar
Database
Server

Ethernet Link
@ 100/1000 Mbps

Data Acquisition

Analog Back End

 Ethernet / OF Network
@ 100/1000 Mbps

Antenna - 30

Antenna - 1

Local
C & M
System

Antenna Switch

VOIP
Phone

Video
Camera

MCM 1
Sentinel
MCM 2
IF System
MCM 3
OF System
Servo / FPS

Figure shows final full fledge TELESET-ABCCOM software chain

There are certain things which we need to do for final system like :
- Ethernet communication between ABCCOM and MCM/SERVO.
- Final design and development of GUI ( Control and Monitor ).
- Interaction with other system like Data acquistion, Correlator, Pulsar, Baseband and MCM analog receiver system.
- Development of Multi-user and Multi-Subarray features in Teleset.
- Some error is there in MJD calculation of ABCCOM program which needs to be sorted out.
- Designing Astronomical display.
- Through testing with performance tuning and software optimization.

How we should proceed
- All requirement has to be gathered from all users like astronomers, engineers operators etc.
- All requirement specifications has to be properly documented.
- After finalizing system requirement document, overall system architecture has to be drawn.
- Proper distribution of functionality between different architectural blocks.
- Communication protocol between different architectural blocks.
- Through testing with performance tuning and software optimization.